## Slide 1
From NCCL to the wire
Each layer has one job. Data skips the kernel
NCCL
MPI
collectives, point-to-point
aws-ofi-nccl
NCCL net plugin -> libfabric
libfabric EFA provider
efa fabric: ordering, large messages
rdma-core libibverbs + efa
queues and doorbells in user space
efa.ko (kernel driver)
setup: queues, memory registration
control path (syscall)
Nitro card: EFA device + SRD (multipath, retransmit, congestion control)
data path: no syscall, no kernel
spine-leaf Ethernet fabric
app
libfabric
rdma-core
kernel
Nitro hardware

## Slide 2
Nitro: I/O moves off the host
The host CPU runs the workload; cards run network and storage
EC2 instance (guest)
host CPU / GPU / Trainium (workload)
ENA / EFA driver
NVMe driver
host: Nitro Hypervisor (CPU and memory only)
Nitro cards (PCIe)
Card for VPC: ENA, EFA, SRD, encryption
Card for EBS: NVMe, encryption
Nitro Controller
SR-IOV VF
SR-IOV VF
workload
guest driver
Nitro

## Slide 3
When a lost packet needs a timeout
TCP waits on the same path; SRD resends fast, and reroutes if the path failed
TCP
send
wait for timeout (min RTO 50 ms in the paper)
resend, same path
SRD
send
fast resend, reroute if failed

## Slide 4
How SRD uses paths on ordinary switches
Switches still hash; the sender changes what they hash
sender's Nitro card
RTT per path
packet header
(encapsulation varies)
switch ECMP hash -> spine 1..4
S1
S2
S3
S4
high RTT -> fewer packets
path failed -> reroute
rate + inflight limit per connection
Nitro hardware

## Slide 5
Measured: SRD stays near ideal
Flow completion time (FCT) relative to ideal. Shalev et al., IEEE Micro 2020
1x
2x
5x
10x
20x
50x
100x
48 flows into one 100 Gb/s link: max FCT
SRD
close to ideal
TCP
3-20x
8 server pairs across racks, uplinks 50% busy
SRD median
+15%
TCP mean
+50%
TCP tail
10-100x

## Slide 6
Setup through the kernel, data straight to the card
Setup when resources are created; the data path on every send
setup (when needed)
create queue pair, completion queue
register memory: pin pages, get a key
map queues and doorbell into user space
libibverbs -> /dev/infiniband/uverbs -> efa.ko
-> admin queue -> device
data transfer (every message)
write work request into the mapped queue
ring the doorbell (MMIO write)
device DMAs from registered memory
poll completion queue in user space
kernel
user space + device

## Slide 7
What the efa fabric adds on top of SRD
libfabric EFA provider. efa-direct skips these protocols
SRD (device)
reliable
unordered
small datagrams
ordering
reorder window per sender (FI_EFA_RECVWIN_SIZE)
large messages
eager / medium / long (CTS) / read protocols
same node
shm provider instead of the NIC
GPU / Trainium memory
HMEM: DMA to accelerator memory (peer to peer)
libfabric EFA provider
device

## Slide 8
Who tells the sender to slow down?
Credits: the receiver says how much it can take. SRD: the sender infers it from ACKs
Credit-based flow control
e.g. InfiniBand link level
Sender
Receiver
data
credits: N free
credits = 0 -> sender waits
receiver decides, explicitly
SRD congestion control
Nitro card, per connection
Sender
Receiver
data
ACK
ACK timing -> delivery rate, RTT per path
sender lowers its own rate and inflight
sender decides, by inference

## Slide 9
How SRD decides it is congested
Shalev et al., IEEE Micro 2020
Inputs
RTT of each path
delivery rate (ACK timing)
own recent send rate
RTT up on one path
that path is busy
-> move packets to other paths
RTT up on most paths
or
delivery rate < send rate
whole connection is congested
(e.g. incast)
-> lower rate limit and inflight limit
goal: fair share with minimum bytes in flight (no queue build-up, no drops as the signal)