## Slide 1
From the PGAS view down to the BAR1 window
Blue: PGAS view. Pink: goes through BAR1. Yellow: NIC. Grey: NVLink (no BAR1). Green: GPU memory
PGAS view: every GPU's symmetric heap in one address book (NVSHMEM)
same node, NVLink
map peer heap, plain store
(no BAR1)
same node, PCIe P2P
map peer heap, plain store
through the peer's BAR1
other node
NIC carries the data
NIC DMA into BAR1
BAR1: GPU memory seen as PCIe addresses
GPU memory (VRAM)

## Slide 2
PGAS: one address book over every GPU's memory
Green: GPU memory. Yellow: the symmetric heap. Pink: a and b, allocated by every PE together
PE 0 (GPU 0)
symmetric heap
a (1 MiB)
b (1 MiB)
PE 1 (GPU 1)
symmetric heap
a (1 MiB)
b (1 MiB)
PE 2 (GPU 2)
symmetric heap
a (1 MiB)
b (1 MiB)
PE 3 (GPU 3)
symmetric heap
a (1 MiB)
b (1 MiB)
a on PE 2 = name + PE number

## Slide 3
"Symmetric" means the same offset from the heap base
Measured on g7.48xlarge, NVSHMEM 3.8.0. Yellow: heap base. Pink: a
default (CUDA VMM)
CUDA VMM disabled
PE 0
heap base
a = 0x10050003600
PE 1
heap base
a = 0x10050003600
PE 0
heap base
a = 0x7f8bc0003600
PE 1
heap base
a = 0x7ff060003600
same value on every PE (by chance)
different values, same tail ...3600

## Slide 4
Can one GPU write another GPU's memory directly over PCIe?
Measured with nvidia-smi topo -p2p rw. Green: OK. Grey: not supported
g6e.12xlarge: 4 × L40S
-
NS
NS
NS
NS
-
NS
NS
NS
NS
-
NS
NS
NS
NS
-
g7.48xlarge: 8 × RTX PRO 4500
-
OK
OK
OK
OK
OK
OK
OK
OK
-
OK
OK
OK
OK
OK
OK
OK
OK
-
OK
OK
OK
OK
OK
OK
OK
OK
-
OK
OK
OK
OK
OK
OK
OK
OK
-
OK
OK
OK
OK
OK
OK
OK
OK
-
OK
OK
OK
OK
OK
OK
OK
OK
-
OK
OK
OK
OK
OK
OK
OK
OK
-
NVSHMEM with 4 PEs: "Peer GPU is not accessible"
NVSHMEM with 4 PEs: maps every peer heap

## Slide 5
BAR1: the window that shows GPU memory on PCIe
Measured on g6e.12xlarge (L40S). Pink: BAR1. Green: GPU memory. Grey: other BARs. Yellow: other PCIe devices
PCIe address space
BAR0 16 MiB: registers
BAR1 64 GiB: window onto GPU memory
BAR3 32 MiB
GPU memory 45 GiB
CPU, NIC, other GPUs
read and write here

## Slide 6
How the NIC reaches GPU memory
Green: GPU memory. Pink: BAR1. Yellow: NIC. Grey: setup before transfers
1. register the heap
with the NIC
2. driver gives
BAR1 addresses
3. NIC remembers
those addresses
NIC
BAR1 address
GPU memory
per transfer: NIC DMA to the BAR1 address

## Slide 7
Small window vs large window
Pink: mapped part of BAR1. Green: GPU memory
BAR1 smaller than memory (Kepler: min 256 MB)
BAR1 holds all memory + reserve
mapped
GPU memory
map only what is registered
BAR1 Used grows, can run out
mapped once at boot: all of memory
GPU memory
static BAR1 (when enabled): registration reuses it
observed on g7.48xlarge: BAR1 Used 0-3 MiB