## Slide 1
EFA software stack: from the app to the EFA device
Blue: user space. Grey: kernel. Yellow: hardware. Pink: SRD link. Solid: data path. Dashed: setup only
App: NCCL / NVSHMEM / MPI
libfabric (efa provider): reorders, splits large messages
rdma-core + efadv: creates the SRD QP
efa kernel driver
EFA device (Nitro hardware)
data path: kernel bypass
setup
user space
kernel
hardware
peer EFA device
SRD: multipath, reliable, unordered

## Slide 2
Without GPUDirect RDMA: a detour through system memory
Green: GPU memory. Blue: system memory. Yellow: NIC and network. Numbers: steps
GPU memory
system memory
(bounce buffer)
NIC
1. CUDA copy
2. NIC DMA read
network

## Slide 3
With GPUDirect RDMA: NIC accesses GPU memory
Green: GPU memory. Yellow: NIC and network. Grey box: not on the data path
Machine A
Machine B
GPU memory
NIC
system memory
NIC
GPU memory
system memory
network
GPU → NIC → NIC → GPU

## Slide 4
BAR1: a window onto GPU memory
Grey: PCIe address space. Green: GPU memory. Yellow: NIC. Pink: BAR1 window. Dashed: maps to
PCIe address space (shared by CPU, NIC, GPU)
BAR1 window
GPU memory (VRAM)
mapped region
NIC
DMA to the window address